## Slide 1
PHOTOVOLTAIC
TECHNOLOGY
Fundamentals / Modules / Quality / Reliability / Systems
FIRSTBUILD / GE • DIY HOME SOLAR TECHNOLOGY OVERVIEW
Prepared by Intuitive Energy | October 2026
Notes: This is a reusable modular curriculum. For a homeowner-focused workshop, use the companion FirstBuild edition. [Sources] Intuitive Energy original presentation branding; technical materials cited throughout. [/Sources]

## Slide 2
COURSE GUIDE
TRAINING
INTUITIVE ENERGY | PV TECHNOLOGY
02
Today’s learning route
A practical technical overview for DIY solar decision-makers.
01 / UNDERSTAND THE TECHNOLOGY
PV fundamentals
From sunlight to DC, watts and modules.
What do module ratings really mean?
02 / CHOOSE RELIABLE HARDWARE
Materials + reliability
Module layers, failure modes, qualification.
Which product details deserve scrutiny?
03 / PLAN A HOME SYSTEM
Design + safety
Inverters, rooftops, code and approvals.
Which decisions require professionals?
Notes: Explain that sections are intended to be selected and re-ordered depending on audience. [Sources] Training program design: Intuitive Energy. [/Sources]

## Slide 3
01 TECHNOLOGY FUNDAMENTALS
TRAINING
INTUITIVE ENERGY | PV TECHNOLOGY
03
PV in four definitions
01
SOLAR CELL
Semiconductor device that converts absorbed photons into DC electric current.
02
PV MODULE
Interconnected cells sealed into an outdoor-rated product.
03
PV ARRAY
Multiple modules connected into strings and/or parallel circuits.
04
PV SYSTEM
Modules plus racking, inverters, protection, wiring and optional storage.
Notes: A module is not a complete solar power system. [Sources] Source: Solar Cell Technologies – Physical Background (Fraunhofer ISE training, provided, pp. 2–4); DOE PV Technology Basics: https://www.energy.gov/cmei/systems/solar-photovoltaic-technology-basics [/Sources]

## Slide 4
01 TECHNOLOGY FUNDAMENTALS
TRAINING
INTUITIVE ENERGY | PV TECHNOLOGY
04
Sunlight: power arriving at the module
Distinguish the sunlight hitting the panel from the electricity it delivers.
IRRADIANCE
Instantaneous sunlight intensity
W/m²
INSOLATION / IRRADIATION
Sunlight energy received over time • kWh/m²/day
Notes: Ask the audience to distinguish a power-rate metric from an energy-over-time metric. A cloud changes irradiance in seconds. Solar resource is integrated over time. [Sources] Source: Solar Cell Technologies – Physical Background (Fraunhofer ISE training, provided, pp. 2–4); DOE PV Technology Basics: https://www.energy.gov/cmei/systems/solar-photovoltaic-technology-basics; DOE Solar Radiation Basics. [/Sources]

## Slide 5
01 TECHNOLOGY FUNDAMENTALS
TRAINING
INTUITIVE ENERGY | PV TECHNOLOGY
05
How a silicon solar cell makes electricity
Photons generate free charge carriers; the cell separates and collects them.
Front contact
n-type emitter / junction region
Silicon absorber (p- or n-type base)
Rear contact
ABSORB
A photon above the silicon bandgap can create an electron–hole pair.
SEPARATE
Junction and selective contacts help separate charge carriers.
COLLECT
Contacts drive usable DC electricity through an external circuit.
Notes: Teaching simplification: real cells differ in junction placement and carrier-selective contacts. The physical principle is absorption, separation, and collection. [Sources] Source: Solar Cell Technologies – Physical Background (Fraunhofer ISE training, provided, pp. 2–4); DOE PV Technology Basics: https://www.energy.gov/cmei/systems/solar-photovoltaic-technology-basics [/Sources]

## Slide 6
01 TECHNOLOGY FUNDAMENTALS
TRAINING
INTUITIVE ENERGY | PV TECHNOLOGY
06
Watts, kilowatts and kilowatt-hours
Power is a rate. Energy accumulates as that power is delivered over time.
W
Instantaneous power
kW
1,000 watts
kWh
Power × time
Example: 2.0 kW × 3 hours = 6.0 kWh
DC comes from the modules; an inverter supplies AC for typical home loads.
Notes: A 400 W panel does not continuously make 400 W. Nameplate power is defined under laboratory conditions. [Sources] Source: Solar Cell Technologies – Physical Background (Fraunhofer ISE training, provided, pp. 2–4); DOE PV Technology Basics: https://www.energy.gov/cmei/systems/solar-photovoltaic-technology-basics [/Sources]

## Slide 7
01 TECHNOLOGY FUNDAMENTALS
TRAINING
INTUITIVE ENERGY | PV TECHNOLOGY
07
What does a module watt rating mean?
STC enables apples-to-apples comparisons; it is not a weather forecast.
1,000
W/m² irradiance
25°C
Cell temperature
AM1.5G
Reference spectrum
STC
A controlled reference point for comparing labeled DC power.
FIELD CONDITIONS
Roof temperature, sunlight angle, shading, soiling and wiring change power.
Notes: Cell temperature is often much hotter than ambient air temperature in sun. Conditions on a roof rarely match STC. [Sources] Source: Solar Cell Quality and Reliability Control (Fraunhofer ISE training, provided, pp. 4–45); Module Characterization and Reliability (provided, pp. 2–46). [/Sources]

## Slide 8
01 TECHNOLOGY FUNDAMENTALS
TRAINING
INTUITIVE ENERGY | PV TECHNOLOGY
08
How weather changes the output
Sunlight largely controls current; hotter cells typically reduce voltage and power.
01
MORE SUN
More light generally raises current and available power.
02
HOTTER MODULE
Voltage drops as cell temperature rises, reducing peak power.
03
SHADOW / SOILING
Localized shading can constrain a whole series string; dirt creates optical loss.
04
SPECTRUM + ANGLE
Air mass, reflection and incidence angle also affect the result.
Notes: Ask: why can a clear cold day produce unusually strong PV power? [Sources] Source: Solar Cell Technologies – Physical Background (Fraunhofer ISE training, provided, pp. 2–4); DOE PV Technology Basics: https://www.energy.gov/cmei/systems/solar-photovoltaic-technology-basics; Source: Solar Cell Quality and Reliability Control (Fraunhofer ISE training, provided, pp. 4–45); Module Characterization and Reliability (provided, pp. 2–46). [/Sources]

## Slide 9
02 CELL TECHNOLOGIES
TRAINING
INTUITIVE ENERGY | PV TECHNOLOGY
09
Cell designs: why architectures evolve
01
PERC
Passivated emitter and rear cell; mature benchmark technology.
02
TOPCon
Tunnel-oxide passivated contact; high-efficiency n-type platform.
03
HJT / SHJ
Silicon heterojunction with thin amorphous-silicon layers.
04
IBC / BACK-CONTACT
Moves electrical contacts to rear to reduce front shading.
Notes: Newer contact concepts aim to reduce recombination and resistive/optical losses. [Sources] Source: Solar Cell Technologies – Crystalline Silicon Solar Cells (Fraunhofer ISE training, provided, pp. 6–26). [/Sources]

## Slide 10
03 MODULE CONSTRUCTION
TRAINING
INTUITIVE ENERGY | PV TECHNOLOGY
10
Anatomy of a PV module
Layers perform different optical, electrical, mechanical and sealing roles.
FRONT GLASS
Low-iron, mechanically durable optical barrier
FRONT ENCAPSULANT
Bonding, insulation, stress transfer
SOLAR CELL CIRCUIT
DC electricity generation + interconnection
REAR ENCAPSULANT
Adhesion and electrical insulation
BACKSHEET / REAR GLASS
Moisture and environmental protection
+ frame, junction box, cables, seals and connectors
Notes: All-layer exploded diagram is newly drawn. Not to scale. Variants include double-glass, frameless and specific polymer stacks. [Sources] Source: Module Production Process (Fraunhofer ISE training, provided, pp. 2–24); PV Technology Training (provided, pp. 6–7, 15–16). [/Sources]

## Slide 11
03 MODULE CONSTRUCTION
TRAINING
INTUITIVE ENERGY | PV TECHNOLOGY
11
Frame, junction box and bypass diodes
The parts you see outside the laminate are essential to electrical safety.
01
FRAME
Supports module edge and transfers mounting loads.
02
JUNCTION BOX
Protects cable terminations and internal circuit connections.
03
BYPASS DIODES
Reduce reverse-bias stress in shaded subcircuits, not all shading loss.
04
CONNECTORS
Require verified mating compatibility and appropriate ratings.
Notes: DIY safety prompt: a bypass diode is not a rapid-shutdown device. Connectors that physically mate may still lack approved compatibility. [Sources] Source: Module Production Process (Fraunhofer ISE training, provided, pp. 2–24); PV Technology Training (provided, pp. 6–7, 15–16).; Source: UL PV Module Certification: https://www.ul.com/services/pv-module-certification; applicable adopted NEC, local building code, utility and AHJ requirements must be verified per project. [/Sources]

## Slide 12
03 MODULE CONSTRUCTION
TRAINING
INTUITIVE ENERGY | PV TECHNOLOGY
12
Series, parallel and shading
Electrical topology is the bridge between cells, modules and the inverter.
SERIES
Voltage adds • Current is constrained
PARALLEL
Currents add when string voltages are compatible.
BYPASS PATHS
Protect subcircuits under mismatch/shading but do not restore lost sunlight.
HOME DESIGN
Respect inverter voltage windows and module temperature extremes.
Notes: The illustrative series schematic does not imply modules should be connected without proper design; rapid shutdown and disconnect rules apply. [Sources] Source: Module Production Process (Fraunhofer ISE training, provided, pp. 2–24); PV Technology Training (provided, pp. 6–7, 15–16).; Source: DOE Solar PV System Design Basics: https://www.energy.gov/cmei/systems/solar-photovoltaic-system-design-basics; DOE Solar PV Technology Basics. [/Sources]

## Slide 13
03 MODULE CONSTRUCTION
TRAINING
INTUITIVE ENERGY | PV TECHNOLOGY
13
How to read a module datasheet
The critical data are more than the headline wattage.
01
Pmax / STC
Nominal peak DC power for the module under reference conditions.
02
Voc, Isc, Vmp, Imp
Voltage/current limits and operating point.
03
Temperature coefficients
Voltage and power changes as the module warms or cools.
04
Mechanical envelope
Dimensions, mass, clamp zones, loading and mounting method.
05
Safety + wiring
Maximum system voltage, fuse rating, fire class, connectors and cable.
06
Warranty + certification
Qualification, product coverage, performance warranty and traceability.
Notes: Strong teaching exercise: show a real datasheet and ask participants to identify Voc, Isc and maximum permissible series-fuse rating. [Sources] Source: Module Production Process (Fraunhofer ISE training, provided, pp. 2–24); PV Technology Training (provided, pp. 6–7, 15–16).; Source: UL PV Module Certification: https://www.ul.com/services/pv-module-certification; applicable adopted NEC, local building code, utility and AHJ requirements must be verified per project. [/Sources]

## Slide 14
04 MANUFACTURING + QUALITY
TRAINING
INTUITIVE ENERGY | PV TECHNOLOGY
14
Electroluminescence: seeing hidden damage
Apply current and use a sensitive camera to inspect cell activity.
Conceptual EL image
CRACKS / ISOLATION
Dark regions can indicate electrically disconnected cell areas.
METALLIZATION
Finger breaks and contacting defects may appear in EL.
IMPORTANT
Interpret images with calibrated conditions and agreed acceptance criteria.
Notes: Illustration is original and schematic, not an actual EL image. EL grading needs product-specific acceptance criteria, lighting/current protocol and trained review. [Sources] Source: Solar Cell Quality and Reliability Control (Fraunhofer ISE training, provided, pp. 4–45); Module Characterization and Reliability (provided, pp. 2–46). [/Sources]

## Slide 15
05 RELIABILITY
TRAINING
INTUITIVE ENERGY | PV TECHNOLOGY
15
What tries to break a solar panel?
Outdoor exposure combines thermal, optical, electrical, chemical and mechanical stresses.
01
THERMAL CYCLING
Daily expansion and contraction stress solder bonds, interfaces and glass.
02
MOISTURE + HEAT
Water ingress can affect polymers, metals and insulation.
03
UV EXPOSURE
Can damage polymer additives, interfaces and certain cell architectures.
04
MECHANICAL LOAD
Wind, snow, handling and hail stress cells, glass and framing.
05
ELECTRICAL BIAS
Potential-induced degradation, leakage and hot spots under specific conditions.
06
SITE ENVIRONMENT
Salt, ammonia, soiling and extreme climates require specific assessment.
Notes: Failures are driven by stress interactions, not one isolated exposure. Certification tests accelerate stress but do not directly certify an exact field lifetime. [Sources] Source: Module Characterization and Reliability (Fraunhofer ISE training, provided, pp. 3–46); Solar Cell Quality and Reliability Control (pp. 43–45). [/Sources]

## Slide 16
05 RELIABILITY
TRAINING
INTUITIVE ENERGY | PV TECHNOLOGY
16
Two essential qualification families
Know what the test series is designed to demonstrate.
IEC / UL 61215
Design qualification / type approval
Representative environmental and mechanical sequences evaluate design robustness and power change.
IEC / UL 61730
Construction + safety qualification
Electrical shock, fire and mechanical safety risks; includes construction rules and prescribed tests.
Notes: Clarify that UL 61730 applies in relevant US certification contexts; verify applicable national deviations and code adoption. Neither test guarantees 25 years with no failure. [Sources] Source: UL PV Module Certification: https://www.ul.com/services/pv-module-certification; applicable adopted NEC, local building code, utility and AHJ requirements must be verified per project.; Source: Module Characterization and Reliability (Fraunhofer ISE training, provided, pp. 3–46); Solar Cell Quality and Reliability Control (pp. 43–45). [/Sources]

## Slide 17
06 HOME SYSTEMS + CODES
TRAINING
INTUITIVE ENERGY | PV TECHNOLOGY
17
A grid-connected home PV system
Solar modules are only one component in a code-compliant electrical system.
PV ARRAY
Produces DC
POWER ELECTRONICS
Controls and converts
HOME LOADS
Use AC energy
UTILITY METER
Tracks grid exchange
Optional storage + hybrid inverter / backup controls
Notes: One-line is conceptual, not a wiring diagram. Grid interactive systems require utility approval, approved equipment, protection, disconnects and commissioning. [Sources] Source: DOE Solar PV System Design Basics: https://www.energy.gov/cmei/systems/solar-photovoltaic-system-design-basics; DOE Solar PV Technology Basics.; Source: UL PV Module Certification: https://www.ul.com/services/pv-module-certification; applicable adopted NEC, local building code, utility and AHJ requirements must be verified per project. [/Sources]

## Slide 18
06 HOME SYSTEMS + CODES
TRAINING
INTUITIVE ENERGY | PV TECHNOLOGY
18
Three common inverter architectures
The best topology depends on roof geometry, shading, monitoring and cost.
STRING INVERTER
Modules feed one or more DC strings to a central inverter.
Simple and often economical for uniform roof exposure.
DC OPTIMIZERS
Module-level DC electronics feed a compatible string inverter.
Supports module-level power management and monitoring.
MICROINVERTERS
DC-to-AC conversion occurs at the module.
Flexible for complex roofs / independent module operation.
Notes: Module-level electronics do not eliminate all electrical hazards; specific equipment and code-compliant rapid shutdown are required. [Sources] Source: DOE Solar PV System Design Basics: https://www.energy.gov/cmei/systems/solar-photovoltaic-system-design-basics; DOE Solar PV Technology Basics.; Source: UL PV Module Certification: https://www.ul.com/services/pv-module-certification; applicable adopted NEC, local building code, utility and AHJ requirements must be verified per project. [/Sources]

## Slide 19
06 HOME SYSTEMS + CODES
TRAINING
INTUITIVE ENERGY | PV TECHNOLOGY
19
Solar + storage: separate three use cases
01
SELF-CONSUMPTION
Shift midday energy to evening consumption.
02
TIME-OF-USE
Charge / discharge in response to tariffs and utility programs.
03
BACKUP POWER
Critical loads require transfer equipment, islanding and system design.
04
GRID SUPPORT
Export, demand response and power quality capabilities vary by utility.
Notes: A battery adds operational flexibility, not unlimited backup. [Sources] Source: DOE Solar PV System Design Basics: https://www.energy.gov/cmei/systems/solar-photovoltaic-system-design-basics; DOE Solar PV Technology Basics. [/Sources]

## Slide 20
06 HOME SYSTEMS + CODES
TRAINING
INTUITIVE ENERGY | PV TECHNOLOGY
20
A rooftop is a design constraint
Assess structure, geometry and maintenance access before panel selection.
STRUCTURE
Capacity, roof condition, fastener detail, wind/uplift and fire classification.
GEOMETRY
Slope, orientation, obstructions, setbacks, walkways and shading.
LIFECYCLE
Roof replacement timing, maintenance and future removals.
Conceptual roof — not a permitted layout
Notes: A professional roof/structural assessment and code-compliant mounting details are project requirements. Diagram is conceptual, not a proposed rooftop layout. [Sources] Source: DOE Solar PV System Design Basics: https://www.energy.gov/cmei/systems/solar-photovoltaic-system-design-basics; DOE Solar PV Technology Basics.; Source: UL PV Module Certification: https://www.ul.com/services/pv-module-certification; applicable adopted NEC, local building code, utility and AHJ requirements must be verified per project. [/Sources]

## Slide 21
06 HOME SYSTEMS + CODES
TRAINING
INTUITIVE ENERGY | PV TECHNOLOGY
21
The regulatory stack for US home solar
Certification, installation code, utility requirements and local permits are separate layers.
01
MODULE + EQUIPMENT
UL 61730 / IEC 61215; inverter and power electronics listings (e.g., UL 1741 as applicable).
02
NATIONAL ELECTRICAL CODE
NFPA 70, especially PV/energy storage articles; edition depends on jurisdiction.
03
ROOF + FIRE + BUILDING
Local structural, building and fire codes, approved mounting details.
04
UTILITY INTERCONNECTION
Utility rules, grid protection, metering and commissioning.
05
LOCAL AUTHORITY / AHJ
Permit submission, inspections, fees and approval to energize.
06
CONTRACTOR / SAFETY
Licensing and qualification requirements for electrical work differ by state / locality.
Notes: This is a framework, not a jurisdiction-specific compliance checklist. Verify local adopted code edition and utility program before procurement. [Sources] Source: UL PV Module Certification: https://www.ul.com/services/pv-module-certification; applicable adopted NEC, local building code, utility and AHJ requirements must be verified per project. [/Sources]

## Slide 22
06 HOME SYSTEMS + CODES
TRAINING
INTUITIVE ENERGY | PV TECHNOLOGY
22
DIY boundary: electrical safety is non-negotiable
A panel exposed to light is an active DC source, even when the utility is down.
DO NOT ASSUME
A breaker turns off a sunlit module.
A bypass diode provides rapid shutdown.
Mated-looking connectors are automatically compatible.
VERIFY WITH YOUR AHJ
Permitting and applicable adopted NEC edition.
Listed equipment and rapid-shutdown design.
Grounding, wiring, roof attachment and fire access.
Licensed electrician / installer responsibilities.
Notes: Convey this clearly to homeowners: this is a technical introduction, not a DIY instruction to handle live DC systems or connect to the grid. [Sources] Source: UL PV Module Certification: https://www.ul.com/services/pv-module-certification; applicable adopted NEC, local building code, utility and AHJ requirements must be verified per project. [/Sources]

## Slide 23
06 HOME SYSTEMS + CODES
TRAINING
INTUITIVE ENERGY | PV TECHNOLOGY
23
A homeowner-safe project workflow
01
1. SITE + LOAD
Gather annual bills, future EV/heat pump loads, roof condition and photos.
02
2. FEASIBILITY
Estimate shade, usable roof area and energy production.
03
3. DESIGN + PERMIT
Qualified design, equipment selection, structural and electrical review.
04
4. INSTALL + VERIFY
Follow local licensing, inspections, utility approval and commissioning.
Notes: The DIY-friendly work is education, site data and design choices—not unqualified energized work. [Sources] Source: DOE Solar PV System Design Basics: https://www.energy.gov/cmei/systems/solar-photovoltaic-system-design-basics; DOE Solar PV Technology Basics.; Source: UL PV Module Certification: https://www.ul.com/services/pv-module-certification; applicable adopted NEC, local building code, utility and AHJ requirements must be verified per project. [/Sources]

## Slide 24
06 HOME SYSTEMS + CODES
TRAINING
INTUITIVE ENERGY | PV TECHNOLOGY
24
Home sizing: a simple example
Illustrative only—replace inputs with actual site and utility data.
9,600
kWh / year of use
1,300
kWh / kWdc / year
7.4
kWdc rough size
Required DC size ≈ annual load ÷ modeled specific yield
Actual design changes with self-consumption goals, net billing, roof area, losses and future loads.
Notes: Example calculation: 9600 / 1300 = 7.38 kWdc. The chosen 1300 kWh/kW-year is an illustrative input, not a Kentucky or national average. [Sources] Source: PVWatts V8 API documentation: https://developer.nlr.gov/docs/solar/pvwatts/v8/; https://pvwatts.nrel.gov/ [/Sources]

## Slide 25
06 HOME SYSTEMS + CODES
TRAINING
INTUITIVE ENERGY | PV TECHNOLOGY
25
US federal homeowner tax-credit update
Current as of October 2026; verify incentives immediately before committing.
SECTION 25D
Ended for post-2025 installations
IRS GUIDANCE
The 30% residential clean energy credit is unavailable for installations completed after December 31, 2025.
ALTERNATIVES
Explore eligible state/local programs and utility incentives; program rules vary.
Notes: Source update verified against IRS public guidance in October 2026. Older training slides included incentives that have since changed. Do not give individualized tax advice. [Sources] Source: Internal Revenue Service Residential Clean Energy Credit: https://www.irs.gov/credits-deductions/residential-clean-energy-credit; IRS Public Law 119-21 FAQs: https://www.irs.gov/newsroom/faqs-for-modification-of-sections-25c-25d-25e-30c-30d-45l-45w-and-179d-under-public-law-119-21-139-stat-72-july-4-2025-commonly-known-as-the-one-big-beautiful-bill-obbb [/Sources]

## Slide 26
06 HOME SYSTEMS + CODES
TRAINING
INTUITIVE ENERGY | PV TECHNOLOGY
26
Home solar: questions to ask before buying
Use these questions to structure a consultation or homeowner workshop.
01
THE ROOF
Will it last as long as the array? Is there a structural review?
02
THE SUN
Is there a defensible shade / energy production model?
03
THE HARDWARE
Is module, inverter, racking and connector compatibility documented?
04
THE SAFETY
Who owns permits, rapid shutdown, wiring, inspection and interconnection?
05
THE MONEY
What is the utility rate, export compensation and all-in installed price?
06
THE LIFETIME
Who handles monitoring, warranty claims, roof removal and maintenance?
Notes: Open discussion. Ask participants to rank their top three risk areas. [Sources] Source: DOE Solar PV System Design Basics: https://www.energy.gov/cmei/systems/solar-photovoltaic-system-design-basics; DOE Solar PV Technology Basics.; Source: UL PV Module Certification: https://www.ul.com/services/pv-module-certification; applicable adopted NEC, local building code, utility and AHJ requirements must be verified per project. [/Sources]

## Slide 27
KEY TAKEAWAYS
TRAINING
INTUITIVE ENERGY | PV TECHNOLOGY
27
The five ideas to take home
Technology choice, installation quality and lifetime behavior are inseparable.
01
Sunlight becomes DC through a semiconductor cell.
02
A module is an engineered stack, not just a silicon wafer.
03
Nameplate watts are a controlled rating—not daily or annual energy.
04
Reliability depends on materials, production, qualification and the site.
05
A safe home system needs qualified design, permits and commissioning.
Notes: Close by asking which part of the PV system creates the greatest perceived risk for the audience. [Sources] Intuitive Energy training synthesis. [/Sources]

## Slide 28
SOURCE ACKNOWLEDGMENTS
TRAINING
INTUITIVE ENERGY | PV TECHNOLOGY
28
Technical references and reuse guidance
An original training synthesis, not a reproduction of another organization’s deck.
PROVIDED MATERIALS
Fraunhofer ISE 2025 training: cell physics / architecture, cell quality, module production, module reliability; Trina–Fraunhofer LCOE study; SolX PV overview (content reference only).
PUBLIC TECHNICAL REFERENCES
U.S. Department of Energy PV basics and system design; UL Solutions PV qualification; PVWatts V8 documentation; IRS 2026 federal credit guidance.
SOURCE RIGHTS
Some supplied Fraunhofer material was marked restricted or confidential. This presentation recreates concepts with new figures; confirm permission before externally distributing sensitive source-derived details.
Notes: References are also in speaker notes on individual slides. Check scope of reuse permissions before public dissemination. [Sources] Source: Solar Cell Technologies – Physical Background (Fraunhofer ISE training, provided, pp. 2–4); DOE PV Technology Basics: https://www.energy.gov/cmei/systems/solar-photovoltaic-technology-basics Source: Solar Cell Technologies – Crystalline Silicon Solar Cells (Fraunhofer ISE training, provided, pp. 6–26). Source: Module Production Process (Fraunhofer ISE training, provided, pp. 2–24); PV Technology Training (provided, pp. 6–7, 15–16). Source: Solar Cell Quality and Reliability Control (Fraunhofer ISE training, provided, pp. 4–45); Module Characterization and Reliability (provided, pp. 2–46). Source: Module Characterization and Reliability (Fraunhofer ISE training, provided, pp. 3–46); Solar Cell Quality and Reliability Control (pp. 43–45). Source: DOE Solar PV System Design Basics: https://www.energy.gov/cmei/systems/solar-photovoltaic-system-design-basics; DOE Solar PV Technology Basics. Source: UL PV Module Certification: https://www.ul.com/services/pv-module-certification; applicable adopted NEC, local building code, utility and AHJ requirements must be verified per project. Source: Analyzing Impact of Modules with Different Wafer Sizes on LCOE, Trina Solar / Fraunhofer ISE webinar (provided, pp. 2–23); project-specific economics are not transferrable without new assumptions. Source: Internal Revenue Service Residential Clean Energy Credit: https://www.irs.gov/credits-deductions/residential-clean-energy-credit; IRS Public Law 119-21 FAQs: https://www.irs.gov/newsroom/faqs-for-modification-of-sections-25c-25d-25e-30c-30d-45l-45w-and-179d-under-public-law-119-21-139-stat-72-july-4-2025-commonly-known-as-the-one-big-beautiful-bill-obbb Source: PVWatts V8 API documentation: https://developer.nlr.gov/docs/solar/pvwatts/v8/; https://pvwatts.nrel.gov/ [/Sources]